## Slide 1
HACKDAY 1.0 · TECH FOR A BETTER TOMORROW
India's heat alerts measure temperature.
Workers collapse on humidity.
ShramShield turns a weather forecast into an enforceable heat-safety shift plan for people who work outdoors:
when to start, how many minutes to work and rest each hour, how much water, and which hours must stop.
shramshield.vercel.app · github.com/sgoel2be24-cyber/shramshield
Solo entry · built in the 8-hour HACKDAY window, 20 September 2026

## Slide 2
THE PROBLEM
Deaths are documented on days when no alert was issued
At least 84 heatstroke deaths, February–July 2025 in a news-based analysis; 7,192 suspected cases against only 14 confirmed (NCDC, via RTI).
Most victims: elderly people, outdoor workers, daily-wage labourers — over 90% of India's workforce is informal, with no mandatory breaks or shade.
HeatWatch's 2025 report recommends WBGT-based alerts and enforceable work-rest cycles; IMD's warnings remain dry-bulb only. A plea is pending before the Supreme Court.
WBGT = 0.7·Tnwb + 0.2·Tg + 0.1·Tdb
Temperature alone cannot express this. A supervisor does not need another readout — they need to know what to do with today's shift.
Sources: HeatWatch “Struck by Heat” (2025); The Hindu; LiveLaw (SC plea, July 2026)

## Slide 3
WHAT IT DOES
One screen: the plan for today's shift
Output | Example — Delhi forecast, moderate work, acclimatised crew
Recommended shift window | 05:00 – 13:00 instead of the default 09:00 rota
Minutes above the limit (8 h window) | 60 min at 05:00 vs 240 min on the 09:00 rota
Work / rest per hour | 53 min work / 7 min rest early → 8 min work / 52 min rest at noon
Water for the crew | litres per worker for that window
Stop-work hours | 11:00–14:00 across the day, very heavy work, real May 2025 Delhi day
Hand-off | Copy plan as text (WhatsApp-ready) · print as a one-page wall sheet
Live forecast, or real bundled data for seven Indian cities and two archived heatwave days —
the demo works with no network and no API key at all.

## Slide 4
PROOF
Same thermometer. Different danger.
Real day, 20 May 2025 | Peak air temp | Peak WBGT | Work permitted (moderate) | Work permitted (very heavy)
Delhi | 42.6 °C | 30.9 °C | 897 min | 310 min, 240 min stopped
Jaisalmer | 42.5 °C | 28.8 °C | 1,167 min | 447 min, no stop hours
Air temperatures within 0.1 °C. Delhi's humidity costs the same crew 270 minutes of permitted work and
pushes very heavy work into a genuine stop-work state. No dry-bulb alert can see that.
76/76 engine tests pass
tsc clean · strict + noUncheckedIndexedAccess
Wet bulb matches Open-Meteo's independent implementation
0.051 °C mean / 0.170 °C worst case over 504 real hours

## Slide 5
WHY THIS IS NOT A CALCULATOR
No instrument. No key. Our own search over the day.
Existing tools need a WBGT meter or manual site readings, or are paid hardware platforms.
ShramShield computes WBGT from a free keyless forecast, then searches candidate start times and ranks them by minutes above the safe limit — answering “when should this crew work?”.
The engine is hand-written and framework-free: WBGT maths, the ACGIH/ISO tables recorded verbatim, the optimiser, with tests that pin table values, physical properties and the demo narrative.
Auditable by design
Every limit traces to a published table, and the app states what is estimated and what is not proven.
Degrades honestly
Live forecast fails → bundled real data, with a visible reason. Never a blank screen or a fake number.
Cheap to run, measured
95 KB in 3 requests, no server, no key, zero API calls unless a live forecast is asked for.

## Slide 6
TRY IT
Open the link, switch two controls
1. The default view: the verdict line — start 05:00, not 09:00.
2. Dataset → Delhi heatwave (May 2025) and Work rate → Very heavy work: the banner names the stop hours inside the shift, the timeline four across the day — a real 2025 day.
3. “Same thermometer, different danger” — the two-city comparison.
4. “How this is computed, and what we have not proven” — standards, assumptions, measured evidence.
shramshield.vercel.app · github.com/sgoel2be24-cyber/shramshield
Advisory tool. Modelled globe and wet-bulb terms, no clothing adjustment, night shift out of scope — stated in the app.